## Slide 1: Line Follower Robot design and implementation
10/22/2016
Ihab Salameh
Grand PrIEEE Competition 2017

## Slide 2: Outline
What is a line follower
Why is it useful
System design and challenges
Expectations and timeline
Resources and logistics
Team selection

## Slide 3: Project description
To design, test and implement a robot that can detect an arbitrary track and race autonomously with a $500 budget

## Slide 4: Introduction
Detects line based on color contrast or freq
Target speed is 10 ft/s
Source: jacobsschoolofengineering.blogspot.com

## Slide 5: Applications
Source: www.google.com/selfdrivingcar/
Source:
http://article.wn.com/view/2015/05/20/Robots_serve_meals_in_China/
Source:
www.youtube.com
Self Driving Cars
Meal Serving
Drink Runner

## Slide 6: System architecture
Motor Driver
(H-Bridge)
Motor
Servo
Battery
(Li-Po)
Encoder
Voltage Regulator
Processing Board
(Arduino/Beagle-Bone)
Line Scan Camera
5V
5V
5V
6V
12V
5V
6V
12V

## Slide 7: Line-Scan Sensor
Parallax TSL1401-DB
Linear array of 128 photodetectors
Outputs analog intensity for each pixel (0V – 5V)
Field of view equal to subject distance
Must meet clock timing requirements (min 5 kHz)
Source: TSL1401-DB Manual

## Slide 8: Line Detection I
Analog data is sampled using BBB’s ADC subsystem
12-bit ADC converts (0-5V) (0-4095) integers
Utilized the Programmable Real-Time Unit (PRU) to meet timing requirements (10 KHz ~ 78 frame/sec)

## Slide 9: Median filter

## Slide 10: Gradient Filter
Look for maximum slopes
Line center determined by
taking the average of those
indices

## Slide 11: Adaptive thresholding
Problem:
  Need to accommodate for different lighting conditions
  Brighter setting requires larger threshold
Solution:
  Width requirement (~ 4-8 pixels) when FOV = 25”
  Set threshold relative to average of all pixel values

## Slide 12: Steering control I
Started with Proportional controller
Moved to Proportional, Integral,
Derivative controller (PID)
Needed to model the system
Chose a geometric model

## Slide 13: Steering control ii
Source: intechopen.com
Source: Snider CMU-RI-TR-09-08
Pure Pursuit method
Bicycle model

## Slide 14: Speed control (h-bridge basics)
Source: ModularCircuits.com

## Slide 15: Speed control I
Designed and tested H-Bridge
Fabricated and soldered PCB
Set Pulse Width Modulation
(PWM) frequency to 20KHz
  Smoother response
  Lower torque ripple

## Slide 16: Speed control II
Used quadrature encoder
Speed based on encoder counts
Calibrated max and min speeds
Used turn curvature to set
reference speed
Source: TI AM335x Manual

## Slide 17: Safety feature: Kill switch
Must be able to stop the car
RF switch and electromagnetic interference
Bluetooth switch
Source: mcuoneclipse.com

## Slide 18: Hardware integration I
3D-printed camera mounts
Aluminum camera mast
Designed platform in SolidWorks
CNC-machined carbon fiber
top plate

## Slide 19: Hardware integration ii

## Slide 20: Testing Results
Achieved speeds exceeding 10.5 ft/s
Small oscillations but consistent stability

## Slide 22: Race results
Did not finish at UCSD’s Grand PrIEEE race
  Camera’s IR filter fell off lens
  Readings were at saturation level
  Beaglebone’s USB port broke during race
Finished 6th place at UC Davis’s NATCAR race
  Performance improved after removing IR filter
  Car hopping
  Loose power connection killed the system in best run

## Slide 23: Lessons learned
Always have backups
Inspect all system components
Fixing issues before proceeding is cheaper
Test under a wide range of conditions

## Slide 24: Team management
Approach
  Explaining overall system design
  Encourage all members to provide input
  Breaking down assignments into manageable chunks
  Tasks vs results
  Utilize all available resources

## Slide 25: Resources
$500 Budget (IEEE) – use it wisely!
Maker Space (www.jacobsschool.ucsd.edu/envision)
IEEE Project Space (EBU1 )
Facebook page
Github (https://github.com/isalameh/GrandPrIEEEE_2017.git)

## Slide 26: Timeline
Fall:
  Week 5: Start meeting with your teams ASAP!
  Week 6: Have system design outline complete (preliminary)
  Week 7: Put in main Purchases (motor driver, sensor, MCU)
  Week 8: Build and test H-Bridge
  Week 9: Design PCB layout, Send for fabrication

## Slide 27: Timeline II
Winter:
  Sensor integration
  Dynamic modeling
  Controller Design
Spring
  Testing, debugging and optimization

## Slide 28: Logistics
Read the competition rules (all team members)
Project lifecycle
ID encoding (Tawnee Gomez)
LiPo Batteries (under consideration)

## Slide 29: Questions